POSSUM VALLEY

MUNICIPAL AUTHORITY

609 Clearview Road

Aspers, Pa 17304

(717)  677-8551

(717)  677-4703 (Fax)

RULES & REGULATIONS

SANITARY SEWER SYSTEM

Adopted August 26, 1985

Revised March 16, 1993

Revised February 12, 2004

Revised December 4, 2008

Revised December 8, 2016

Revised January 5, 2017

Revised September 9, 2021

Revised January 13, 2022

# TABLE OF CONTENTS

Resolution……………………………………………….................................................3

## Section I

Definitions………………………………………………………….................................4

Building Sewers and Connections. ……………………………………………………7

Building Sewers and Connection to Sewers………………………..............................8

Prohibited Wastes and Industrial Wastes…………………………………………….8

Regulations Governing Admission of Industrial Wastes

Into the Sewage Collection system…………………………………………….11

Access………………………………………………………………...............................14

Installation of Building Sewer………………………………………………………...15

## Section II

Solids Retaining Tanks & Pumping Stations………………………………………...21

## Section III

Capital Charges Fee for Sewer Service………………………………………………22

## Section IV

Sewer Rentals or Charges…………………………………………..............................23

Time and Method of Payment………………………………………………………...25

Change in Address, Ownership or Tenancy…………………………………………26

Enforcement……………………………………………………….…………………...26

## Section V

Additional Provisions of this Resolution…………………………..............................27

POSSUM VALLEY MUNICIPAL AUTHORITY

ADAMS COUNTY, PENNSYLVANIA

RESOLUTION

IMPOSING RATES, RULES AND REGULATIONS GOVERNING SEWER SERVICE WHEN OBTAINED FROM THE SEWER SYSTEM OF THIS AUTHORITY; CHARGING A CONNECTION FEE PROVIDING FOR THE PAYMENT OF SUCH CONNECTION FEE; IMPOSING A CHARGE FOR SEWER CAPACITY RESERVED; PROVIDING FOR THE PAYMENT AND COLLECTION OF SUCH CHARGES; AND IMPOSING SEWER RENTAL AND CHARGES FROM THE OWNER OF EACH IMPROVED PROPERTY WHICH SHALL BE CONNECTED TO THE SEWER SYSTEM; OWNERSHIP TRANSFER FOR CURRENT OR REQUIRED COMMERCIAL PUMP STATIONS

WHEREAS, this Authority, pursuant to authority vested in it by law, plans to construct and operate a complete sanitary sewage system for rendering sewage service for certain portions of the Borough of Bendersville (The “Borough”) and certain portions of the Township of Menallen all of which facilities, together with all additions, extensions and improvements which may be made or acquired from time to time, are referred to as the “Sewer System”;

and

WHEREAS, this Authority has power and authority to impose Rules and Regulations governing sewer service when obtained from the Sewer System of the Authority; and

WHEREAS, this Authority has power and authority to charge a connection fee whenever the owners of any property connects such property with a sewer main of the Authority, as provided in the Pennsylvania Municipality Authorities Act, as amended and supplemented, and desires to impose and charge Capital Charges Fee; and

WHEREAS, this Authority has power and authority to impose sewer rentals or charges for use of the sewage facilities owned and operated by this Authority and for collecting, transporting and treatment of waste discharges thereto, and providing a method of payment for such sewer rentals or charges.

NOW, THEREFORE, BE IT RESOLVED, by the Board of this Authority, as follows:

SECTION I

RULES AND REGULATIONS

SEWER SYSTEM

Definitions:  Unless the context specifies and clearly indicated otherwise, the 	meaning of items and phrased pertaining to this Resolution shall be as follows:

A. “Authority” means Possum Valley Municipal Authority, a Pennsylvania 	municipality authority.

B. “B.O.D.” (Biochemical Oxygen Demand) means the quantity of oxygen expressed 	in ppm.  Utilized in the biochemical oxidation of organic matter under standard 	laboratory procedure for 5 days at 20 degrees Centigrade.  The standard laboratory 	procedure shall be that found in the latest edition of “Standard Methods for the 	Examination of Water and Wastewater: published by the American Public Health 	Association.

C. “Borough” means the Borough of Bendersville, Adams County, Pennsylvania, 	acting by and through its Borough Council.

D. “Building Drain Clean-out” means a clean-out on the building drain just inside 	or outside the building wall through which the sewer may be cleaned.  In the case of 	existing construction a clean-out shall be located on the Service Line.

E. “Building Sewer” means the extension from the sewage drainage system of any 	structure to the Lateral of the Sanitary Sewer System.

F. “Building Trap” means a device, fitting or assembly of fittings installed on the 	building drain to prevent circulation of air between the drainage system of the building 	and the Service Line.  In the case of existing construction, the Building Trap shall be 	located on the Service Line.

G. “Capital Charges” means fees to be paid for new connection to the Sewer System or 	those customers increasing their need for Sewer capacity.  Fees are to be calculated in accordance 	with the Municipal Authorities Act and be duly adopted by the Authority

H. “Cellar Drain” means a protected and trapped drain for the purpose of carrying off 	spent water from the basement of a dwelling, factory, laboratory, workshop or other 	building, but excluding any drainage from rain water, springs, wells, or other ground or 	surface water.

I. “Developer” means any landowner who makes or causes to be made a subdivision 	of land or a land development.

J. “Department of Environmental Protection” means the Department of 	Environmental Protection of the Commonwealth of Pennsylvania, or its successor in 	authority.

K. “DEP Permit” means the permit(s) which is required by the Department of 	Environmental Protection of the Commonwealth of Pennsylvania for the construction of 	a new sanitary sewer 	line or the extension of an existing sanitary sewer system.

L. “Dwelling Unit” means a building under one roof and occupied by one family or 	one business; or

1. A combination of buildings in one enclosure or group and occupied by one 			family or one business; or

2. One side of a double building or house having a solid vertical partition wall; or

3. Each room or group of rooms in a building occupied or intended for occupancy 			as a separate business or as separate living quarters by a family or other group of 			persons living together or by a person living alone; or

4. Each apartment, office or suite of offices in a building or house having several 			such apartments, offices or suites of offices and using in common one or more 			hallways and one or more means of entrance; or

5. Any trailer or mobile home occupied by one family or business: or

6. Any other unit or category listed in the schedule of EDU’s set in Section III.

M. “Fresh Air Vent” means a direct connection leading from the Building Trap to the 	outer air.  In the case of existing construction, the Fresh Air Vent shall be located outside 	the building.

N. “Improved Property” means any property located within this Township and/or 	Borough upon which there is erected a structure intended for continuous or periodic 	habitation, occupancy or use by human beings or animals and from which structure 	Sanitary Sewage and/or Industrial Wastes shall be or may be discharged.

O. “Inspection Port” means the aperture utilized at or near the septic tank to inspect the flow of sewage from the building to the tank.  In the event of a blockage in the line the inspection port is checked for blockage.  If the port is clear then the blockage is in the owners sewer lateral and the owners responsibility to have cleaned by an authorized plumber at their expense.

P. “Industrial Establishment” means any room, group of rooms, building or other 	enclosure used or intended for use in the operation of one business enterprise for 	manufacturing, processing, cleaning, laundering or assembling any product, commodity 	or article, or from which process waste, as distinct from Sanitary Sewage, shall be 	discharged.

Q. “Industrial Wastes” means any and all wastes and wastewaters discharged from 	an Industrial Establishment other than Sanitary Sewage.

R. “Land Development” means the improvement of one lot or two or more 	continuous lots, tracts or parcels of land for any purpose involving (1) a group of two or 	more buildings, or (2) the division or allocation of land or space between or among two 	or more existing or prospective occupants by means of, or for the purpose of streets, 	common areas, leaseholds, condominiums, buildings groups or other features, or (3) any 	other project requiring the approval of the Township or the Borough pursuant to any Act 	or Ordinance.

S. “Planning Module for Land Development” means the Modules or the 	Planning Module Exemption as required by the Pennsylvania Department of 	Environmental Protection under Act 537, the Pennsylvania Sewage Facilities Act.

T. “Lateral” means that part of the Sewer System extending from a Sewer to the curb 	line, or if there shall be no curb line, to the property line or, if no such Lateral shall be 	provided, then ”Lateral” shall mean that portion of or place in a Sewer which is provided 	for connection of any Building Sewer.

U. “Owner” means any Person vested with ownership, legal or equitable, sole or 	partial, of any Improved Property.

V. “Person” means any individual, partnership, company association society, 	corporation or 	other group or entity.

W. “pH” means the logarithm of the reciprocal of the concentration of hydrogen ions, 	expressed in grams per liter of solution, indicating the degree of acidity or alkalinity of a 	substance.

X. “Plumbing Inspector” means the person or persons appointed by the Authority 	to enforce the terms of these Rules and Regulations.

Y. “Sanitary Sewage” means normal water-carried household and toilet wastes from 	any Improved Property.

Z. “Sewer” means any pipe or conduit constituting a part of the Sewer System used or 	usable for sewage collection purposes.

AA. “Sewer System” means all facilities as of any particular time, for collecting, 	pumping, transportation, treating or disposing of Sanitary Sewage and Industrial Wastes, 	to be owned by the Authority

BB. “Solids Retaining Tank” means a concrete, watertight tank designed to receive 	wastewater from a home or business, provide solid/liquid separation provide solids 	storage and to allow clarified liquid discharge for further treatment and disposal.

CC. “Storm Sewer or Drain” means a pipe or conduit which carries storm, surface 	water, 	drainage and certain industrial waste discharges, such as cooling and air 	conditioning water.

DD. “Subdivision” means the division of a single lot, tract or parcel of land, or part 	thereof, into two or more lots, tracts or parcels of land, including charges in street lines or 	lot lines for the purposes, whether immediate or future, of improvement and 	development.

EE. “Suspended Solids” means Suspended Solids as determined pursuant to the 	procedure set forth in the latest edition of “Standard Methods for the Examination of 	Water and Wastewater published by the American Public Health Association.

FF. “Township” means the Township of Menallen, Adams County, Pennsylvania, 	acting by and through its Board of Supervisors.

BUILDING SEWERS AND CONNECTIONS

A. No Person shall uncover, connect with, make any opening into or use, alter or disturb, 	in any manner any Sewer or the Sewer System without first making application for and 	securing a permit, in writing, from this Authority.

B. Application for a permit shall be made by the Owner of the Improved Property to be 		served or his duly authorized agent.

C. No Person shall make, or cause to be made, a connection of any Improved Property to 	the Sanitary Sewer System until such Person shall have fulfilled each of the following 	conditions:

1. Such Person shall have notified the Authority of the desire and intention to 			connect such Improved Property to a Sewer.

2. Such Person shall have paid to the Authority any fee charged and imposed by 			the Authority, as required under Section II of these Rules and Regulations.

3. Such Person shall have given the Authority at least 24 hours notice of the time 			when such connection will be made so that this Authority may supervise and 			inspect the work of connection and necessary testing.

D. Each Improved Property shall be connected separately and independently with a 	Sewer through a Building Sewer.  Grouping of more than one Improved Property on one 	Building Sewer shall not be permitted, except under special circumstances and for good 	sanitary reasons or other good cause shown, and then only after special permission of this 	Authority, in writing, shall have been secured and subject to such rules, regulations and 	conditions as may be prescribed by this Authority.

E. All costs and expenses of construction of a Building Sewer and all costs and expenses 	of connection of a Building Sewer to a Sewer shall be borne by the Owner of the 	improved Property to be connected; and such Owner shall indemnify and save harmless 	the Township, the Borough, and the Authority, from all loss or damage that may be 	occasioned, directly or indirectly, as a result of construction of a Building Sewer or of 	connection of a Building Sewer to a Sewer.

F. A Building Sewer shall be connected to a Sewer at the place designated by this 	Authority and where the Lateral is provided.  The invert of a Building Sewer at the point 	of a gravity connection shall be at the same or higher elevation than the invert of the 	Sewer, unless the connection is a pressure connection from a force main discharge, as 	approved by this Authority.  The connection of a Building Sewer to the Lateral shall be 	made secure and watertight.

G. Acquisition of any and all easements or right-a-ways needed to connect an Improved 	Property to the Public Sewer shall be the sole responsibility of the Owner of such 	Improved Property.

F. Every Building Sewer of any Improved Property shall be maintained in a sanitary and 	safe operating condition by the Owner of such Improved Property.

G. Every excavation for a Building Sewer shall be guarded adequately with barricades 	and lighted to protect all Persons from damage and injury.  Streets, sidewalks and other 	public property disturbed in the course of installation of a Building Sewer shall be 	restored, at the cost and expense of the Owner of the Improved Property being connected, 	in a manner satisfactory to this Authority.

H. If any Person shall fail or refuse, upon receipt of a notice of this Authority, in writing, 	to remedy any unsatisfactory condition with respect to a Building sewer, within 60 days 	of receipt of such notice, this Authority may refuse to permit such Person to discharge 	Sanitary Sewage and Industrial Wastes into the Sewer System until such unsatisfactory 	condition shall have been remedied to the satisfaction of the Authority.

BUILDING SEWERS AND CONNECTIONS TO SEWERS

A. Where an Improved Property, at the time of connection to a Sewer is required, shall be 	served by its own sewage disposal system or device, the existing house sewer line shall 	be broken on the structure side of such sewage disposal system or device and attachment 	shall be made, with proper fittings, to continue such house sewer line, as a Building 	Sewer.

B. No Building Sewer shall be covered until it has been inspected and approved by this 	Authority.  If any part of a Building Sewer is covered before so being inspected and 	approved, it shall be uncovered for inspection at the cost and expense of the Owner of the 	Improved Property to be connected to a Sewer.

PROHIBITED WASTES AND INDUSTRIAL WASTES

A. No Person shall discharge or cause to be discharged any storm water, surface water, 	spring water, ground water, roof runoff, and subsurface drainage, building foundation 	drainage, cellar drainage, drainage from roof leader connections and overflow or drainage 	from cesspools into any Sewer.

B. This Authority reserves the right to refuse permission to connect to the Sewage 	System, to compel discontinuance of use of the Sewage System, or to compel 	pretreatment of Industrial Wastes, in order to prevent discharges deemed harmful or to 	have a deleterious effect upon any Sewer, the Sewage System or the Wastewater 	Treatment Plant.

C. No Sanitary Sewage or Industrial Wastes shall be discharged to the Sewage Collection 	System:

1. Being harmful or deleterious to the Sewage System.

2. being inhibitory to the treatment process at the sewage treatment plant 				constituting part of the Sewage Disposal System.

3. Containing any gasoline, benzene, naphtha, fuel oil or other flammable or 			explosive liquids, solids or gases.

4. Carry fats, oils or greases in excess of 50 mg/l by weight.

5. Being discharged into the Sewage System at temperatures in excess of 105 			degrees F.

6. Being discharged into the Sewage System in batches of such volume as to tax 			the capacity of the Sewage System or adversely affecting the treatment process of 			the Sewage Disposal System.

7. Being of such color or other characteristic as to require special treatment to 			render the resulting effluent of the sewage treatment plant constituting part of the 			Sewage Disposal System acceptable for discharge to the receiving stream.

8. Being food wastes, garbage (unless treated in an approved manner), vegetable 			or fruit rinds, or paunch manure, feathers, bones, rags or any other solid, fibrous 			or viscous inorganic or organic substances which the Sewage System or Sewage 			Disposal System is not intended to receive.

9. Being of such character, concentration, volume or combination as to tax the 			capacity of the sewage treatment plant constituting part of the Sewage Disposal 			System.

10. Including synthetic, organic detergents or similar compounds in such volume 			as to interfere with the treatment process or the satisfactory operation of the 			sewage treatment plant constituting part of the Sewage Disposal System.

11. Including any liquids having a pH exceeding a minimum value of 6.0, or a 			maximum of 9.0, or found to be excessively corrosive.

12. Including any waters or wastes with a B.O.D. in excess of 225 mg/l by weight, 		unless 	otherwise approved in accordance with the surcharge formula.

13. Including any waters or wastes with a Suspended Solids content in excess of 			275 mg/l by weight, or containing Suspended Solids of such character and /or 			quantity that unusual attention or expense is required to handle and /or treat such 			materials, unless otherwise approved in accordance with the surcharge formula.

14.  Any water or waste containing any Toxic Substance, as defined below, in 			quantity sufficient to constitute a hazard to humans or animals or to interfere with 			any wastewater treatment process of the wastewater treatment plant or that will 			pass through the wastewater treatment plant in such condition so that it will 			exceed State, Federal or other validly exiting requirements.  Samplings taken to 			determine the maximum allowable concentration shall be at the point of discharge 		to the Sanitary Sewer System.

Toxic wastes shall include, but not be limited to the following:

Toxic Inorganic Substances			Max. Allowable Concentration

Aluminum (ionic form)		    	   		10.0 mg/l

Antimony						1.0 mg/l

Arsenic							0.1 mg/l			    			Barium							5.0 mg/l						Beryllium						1.0 mg/l						Boron							1.0 mg/l

Cadmium						0.02 mg/l					Chlorides						250 mg/l

Chromium, total						1.0 mg/l	       					Chromium (Hexavalent)					0.05 mg/l

Copper							0.5 mg/

Cyanide (total)						0.1 mg/l

Fluorides						1.5 mg/l

Iron							3.0 mg/l

Lead							0.05 mg/l

Manganese						3.0 mg/l

Mercury							0.002 mg/l

Nickel							0.5 mg/l

Selenium						0.1 mg/l

Silver							0.1 mg/l

Sulfate							360 mg/l

Tin							5.0 mg/l

Zinc							0.3 mg/l

Organic Compounds/Pollutants	        Max. Allowable Concentration

Acetone							50.0 mg/l

Acrolein							0.2 mg/l

Acrylonitrile						0.2 mg/l

2, 4-dinitrophenol					0.5 mg/l

2-methyl-4, 6-dinitrophenol				0.5 mg/l

Alcohols (Total)						25.0 mg/l

Benzidine						50.0 mg/l

Chlorinated Hydrocarbons (Total)			       	2.0 mg/l

Chloroform						.01 mg/l

Ethylbenzene						1.0 mg/l

Hexachlorobenzene					2.0 mg/l

Pesticides & Herbicides (Total)			      	0.1 mg/l

MBA’s (Detergent)					1.0 mg/l

Methylene blue						50.0 mg/l					Methylene Chloride					0.2 mg/l

Organic Compounds/Pollutants	         Max. Allowable Concentration

Naphthalene						1.5 mg/l

Phenols							0.01 mg/l

Total Toxic Organics (TTO)				2.0 mg/l

Toluene							1.0 mg/l

15. Including any water or wastes with a total nitrogen in excess of 80 mg/l, by 			weight, or ammonia nitrogen in excess of 50 mg/l, unless otherwise approved in 			accordance with the surcharge formula.

16. Including any water or wastes with color (Platinum Cobalt Units) in excess of 			75.

17. Including any water or wastes with C.O.D. in excess of 500 mg/l (Surcharge 			will apply above 500 mg/l.)

18. Including any water or wastes with a total phosphorus in excess of 10 mg/l, by 		weight.

19. Including any waste having a chlorine demand in excess of ten (10) mg/l.

20. Including any ashes, cinders, sand, mud, straw, shavings, metal, glass, fur, 			plastics, wood, butcher’s offal, hair or any other solids or viscous substance 			capable of causing obstruction to the flow in sewers or the interference with the 			proper operation of the sewer system.

21. Including any inert, insoluble solids such as asphalt, clay, slag and mill scale, 			or sludge’s and slurries.

22. Including any waters or waste containing radioactive isotopes.

23. Any liquids, solids or gases which by reason of their nature or quantity are, or 			may be, sufficient either alone or by interaction with other substances to cause fire

or explosion or be injurious in any other way to the Wastewater Treatment 			Facility or to the operation of the Wastewater Treatment Facility.  At no time, 			shall two successive readings on an explosion hazard meter, at the point of 			discharge into the system (or at any 	point in the system) be more than five 			percent (5%) nor any single reading over ten percent (10%) of the Lower 				Explosive Limits (LEL) of the meter.  Prohibited materials 	include, but are not 			limited to , gasoline, fuel oil, kerosene, naptha, benzene, toluene, xylene, ethers, 			bromates, carbides, hydrides and sulfides and any other substances which the 			Borough or Township, the Commonwealth or the E.P.A. has notified the User is a 		fire hazard or found to be detrimental to the treatment process.

24. Any wastewater containing any substances which are not amenable to 				treatment or reduction by the biochemical wastewater treatment processes 				employed or are amenable to the treatment only to such a degree that the effluent 			of the sewage treatment works cannot meet the requirements of agencies having 			jurisdiction over the discharge to the 	receiving stream.

25. Any toxic substance not mentioned in the above list that will pass through the 			treatment works and exceed the maximum permitted levels for such substance 			under the requirements of state or other governmental agencies.

26. Including any substance prohibited by any permit issued by the 				Commonwealth of Pennsylvania.

27. Upon the promulgation of the Federal Categorical Pretreatment Standards for 			a particular industrial subcategory, the Federal Standard, if more stringent than 			limitations imposed under this regulation for sources in that subcategory, shall 			immediately supersede the limitations imposed under this regulation.  The 				Authority shall notify all affected Users of the applicable reporting requirements 			under 40 CFR, Section 403.12.

D. Where necessary all Owners shall install suitable pretreatment facilities, including 	grease traps, in order to comply with above paragraph.

Plans, specifications and any other pertinent information relating to proposed facilities for 	pretreatment and handling of wastes shall be submitted for approval of this Authority; 	and no construction of any such facility shall be commenced until approval thereof first 	shall have been obtained from any governmental body having jurisdiction.

Whenever facilities for pretreatment and handling of wastes shall have been provided by 	any Owner, such facilities continually shall be maintained, at the expense of such Owner, 	in satisfactory operating condition and this Authority shall have access to such facilities 	at reasonable times for purposes of inspection and testing.

E. Nothing contained in these Rules and Regulations shall be construed as prohibiting 	any special agreement or arrangement between this Authority and any Person whereby

Industrial Wastes may be admitted into the Sewage System by this Authority, after 	pretreatment and/or appropriate surcharge.

REGULATIONS GOVERNING ADMISSION OF

INDUSTRIAL WASTES INTO THE SEWAGE COLLECTION SYSTEM

A. No Person shall discharge or cause to be discharged into the Sewage System any 	Industrial Wastes except upon application to this Authority and upon receipt of a written 	permit therefore by this Authority.

B. Required Survey Data.  Any Person desiring to make or use a connection to the 	Sewage System through which Industrial Wastes shall be discharged into the Sewage 	Collection System shall file with this Authority an “Industrial Wastes Questionnaire:, to 	be furnished by this Authority, which shall supply to this Authority pertinent data 	including estimated quantity of flow, characteristics and constituents, with respect to 	Industrial Wastes proposed to be discharged into the Sewage System.  The cost of 	obtaining all such data shall be borne by the Person desiring to make or use a connection 	to the Sewage System.

C. Control Manholes.  Any Person who shall discharge Industrial Wastes into the Sewage 	System, when required by this Authority, shall construct and thereafter properly shall 	maintain, at his own expense, a suitable control manhole and other devices as may be 	required by this Authority to facilitate observation, measurement and sampling by this 	Authority of Industrial Wastes discharged to the Sewage System.  Any such control 	manhole, when required by this Authority, shall be constructed at an accessible, safe, 	suitable and satisfactory location in accordance with plans approved by this Authority 	prior to commencement of construction.

D. Changes in Type of Wastes.  Any Improved Property discharging Industrial Wastes 	into the Sewage System and contemplating a change in the method of operation which 	will alter the characteristics and/or volumes of wastes at the time being discharged into 	the Sewage Collection System will notify this Authority, in writing, at least sixty (60) 	days prior to consummation of such charge.

E. This Authority reserves the right to require Improved Properties having large variation 	in rates of waste discharge to install suitable regulating devices for equalizing waste 	flows to the Sewer System.

F. Where required, by the Authority, the user shall provide at his expense such 	preliminary treatment or handling as may be necessary to modify the objectionable 	characteristics or control the quantities and rates of discharge of such water or wastes as 	necessary to reduce B.O.D. to 225 mg/l, suspended solids to 275 mg/l and total solids to 	600 mg/l, or modify the objectionable characteristics to constituents to come within the 	maximum limits provided for in these Rules and Regulation.

Plans, specifications, an any other pertinent information relating to proposed preliminary 	treatment or handling facilities shall be submitted for the approval of the Authority and 	no construction of such facilities shall be commenced until written approval is obtained.

Where preliminary treatment facilities are provided, they shall be maintained 	continuously in satisfactory and effective operation at the User’s expense.  The Authority 	and/or its authorized representatives shall have continuous access to any preliminary 	treatment facilities for inspection.  Operations of and discharges from said facilities shall 	be subject to the requirements of all applicable Federal, State and local codes, ordinances, 	laws and regulations.  Operation and testing data from the pretreatment facilities shall be 	submitted to the Authority each week.

Industrial waste being discharged into the sewer system shall be subject to periodic 	sampling, testing and inspection.  The analyses of samples so obtained shall be the basis 	for computing additional charges in accordance with subparagraph L of this section 	governing admission of industrial waste into the Sewage Collection System.

All sample analysis shall be performed by a laboratory certified by the U.S. 	Environmental Protection Agency and in accordance with the latest edition of “Standard 	Methods for the Examination of Water and Sewage: published by the American Public 	Health Association, AWWA, and the WEF.

A normal sampling schedule including the analyses to be performed on the samples shall 	be included in the Industrial Waste Acceptance Agreement.  The cost of this sampling 	and testing shall be borne by the User and shall be shown as separate charges on the 	user’s sewer bills.

The Authority reserves the right to perform more frequent sampling and analyses at its 	own cost.

A user subject to periodic sampling may request that samples be taken in addition to the 	normal periodic samples taken by the Authority.  The cost of this sampling and analysis 	shall be borne by the User in addition to the cost for normal sampling and analysis.

G.  Any tank truck or any equipment used or intended to be used for the removal, 	transportation, and disposal of sewage and industrial wastes shall conform to the 	following requirements:

1.  The container shall be water tight.

2.  Tanks, containers, or other equipment shall be so constructed that every 			portion of the interior and exterior can be easily cleaned and shall be kept in the 			clean and sanitary condition.

3.  Piping, valves and permanent or flexible connections shall be accessible and 			easily disconnected for cleaning purposes.

4.  The inlet opening, or openings to every container, shall be so constructed that 			the material will not spill outside during filling, transfer, or transport.

5.  The outlet connections shall be so constructed that no material will leak out, 			run out to other than the point of discharge, and shall be of a design and type 			suitable for the material handled and capable of controlling the flow or discharge 			without spillage undue spray, or flooding immediate surroundings while in use.

6.  No connection shall be made at any time between a tap hydrant or outlet 			furnishing potable water on any premises and any container or equipment holding 			waste material by any means other than an open connection.

The sewage and wastes discharged by the tank trucks into the sewer system shall 			not contain industrial waste, chemicals, or other matter, with or without pre-			treatment that does not conform to the requirements of these Rules and 				Regulations.

Any sewage and industrial water to be discharged from tank trucks to the Sewer 			System shall be disposed of at the location designated by the Authority at the time 		or times fixed by the Authority.  All such discharges shall be subject to the written 		consent of and pursuant to written agreement of the Authority.

H.  No provisions of these Rules and Regulations shall be construed as preventing any 	special arrangement or agreement between the Authority and any Person whereby an 	industrial waste of unusual strength or character may be accepted by the Authority for 	treatment, subject to payment therefore by the Person concerned.

I.  Whenever a permitted User shall fail to comply with the rules and regulations of the 	Authority regarding industrial waste, the Authority may revoke the User’s permit and 	take whatever action is necessary to protect the Authority’s sewer system and treatment 	plant including without limitation capping the User’s line and preventing the discharge

into the Authority’s system.

J.  This Authority requires that all discharges of industrial waste will submit to this 	Authority a daily record of metered flows along with a daily analysis of the discharge 	using an analytical method in accordance with references of “Standard Methods, for the 	Examination of Water and Wastewater”.  (AWWA)  (WEF)

K.  This Authority reserves the right to impose surcharges in connection with any 	Industrial Wastes discharged into the Sewage system either by agreement with the Owner 	of the Improved Property or by modifications or alterations hereto.

L.  Basis for setting forth surcharges on Industrial shall be on strength in excess of the 	threshold limits of 225 mg/l for BOD5, 275 mg/l for Suspended Solids, Total Phosphorus 	of 10 mg/l, and 50 mg/l for Ammonia Nitrogen.  Surcharge rates shall be based on a unit 	cost per pound for waste in excess of these threshold limits.

In order to determine the additional charge for Industrial or Commercial Wastewaters 	with strength greater than that of domestic sewage, the following formula shall be used:

Monthly Surcharge = 0.00834 MI 	(BODI – 225) A + (SSI – 275) B

(P-10) C+ (NH3-N – 50) D

Where:	 0.00834 is a constant to convert waste strength express in mg/l to thousand 		pounds of waste.

QI = quarterly industrial waste flow expressed in million gallons.

BODI – 5 day BOD in mg/l of the Industrial or Commercial Waste.

SSI = Suspended Solids of Industrial or Commercial Waste in mg/l.

P = Total Phosphorus of Industrial or Commercial Waste in mg/l.

NH3-N = Ammonia Nitrogen of Industrial or Commercial Waste in mg/l.

225, 275, 10 and 50 = constants expressing waste load strength in mg/l 				for the 	respective pollution parameters.

A, B, C, and D = costs of treating 1,000 pounds of waste at the Authority’s 			wastewater treatment facility for the respective pollution parameters.  				These costs will change as operating costs increase, as capital additions 				are made or as flow at the facility changes.

When a value for BOD, suspended solids, Phosphorus, and Ammonia Nitrogen is less 	than the maximum allowable concentration set forth in the Industrial Waste Surcharge 	Formula, the maximum allowable concentration shall be used in the calculation of the 	Industrial Waste Surcharge.

ACCESS

This Authority or its authorized representative (Plumbing Inspector) shall have the right of access at reasonable times to any part of any Improved property served by the Sewage Collection System as shall be required for purposes of inspection, measurement, sampling and testing and for performance of other functions relating to service rendered by this Authority through the Sewage System.

INSTALLATION OF BUILDING SEWER

Building Sewer or Service Line shall be subject at all times to the inspection and 	approval of the Authority or its duly authorized representative who shall have supervision 	and control over the same.

A.  Size – Service Lines shall in no case be less than four inches in diameter.  Where 	double or multiple homes are permitted to be served by a common line under a special 	connection permit issued by the Authority, the double and multiple homes may be served 	with a four inch line, unless a larger line for a multiple home is required by the Plumbing 	Inspector.  An approved adaptor connecting the Service Line to the Lateral Sewer must 	be used.

B.  Material – Pipe used for Building Sewers or Service Lines shall conform to one of the 	following:

1.  Solid wall PVC sewer pipe SDR (as listed herein) with a single socket “O” ring rubber 	gasket 	joint made in accordance with manufacturer’s recommendations.

2. Recommendations for PVC pipe:

Gravity Sewers:	8” Diameter - SDR 35

6” Diameter - SDR 35 or SDR 26

4” Diameter - SDR 26

Pressure Sewers:	6” Diameter - SDR 21

4” Diameter and Less - SDR 21

3.  UNDERGROUND PIPING OUTSIDE BUILDINGS – The building sewer shall be 	SDR 26 PVC pipe with rubber gasket joints. The pipe shall have a minimum inside 	diameter of four inches.

4.  NEW UNDERGROUND PIPING PASSING THROUGH OR UNDER BUILDING 	SLABS- Only when authorized by an Authority Representative, may a property owner 	install a building sewer beneath a building or slab.  The building sewer shall be SDR 26 	PVC pipe with rubber gasket joints.

Owners wanting to connect the new building sewer to an existing building sewer, shall

demonstrate to the Authority the satisfactory condition of the existing building sewer 	through visual inspection and air testing.  Approval to connect to the existing building 	sewer shall be noted on the connection permit.  If the existing building sewer does not 	meet the Authority’s requirements for Inspection and air testing, connection of the new 	building sewer shall be made as close to the structure as possible.  Connection of the new 	building sewer to the existing building sewer shall be made with approved transition 		fittings resulting in infiltration free construction.

Pipe shall be installed to prevent the admission of groundwater, shall be laid at a 	minimum grade of ¼ inch per foot with the best possible alignment, and shall have the 	maximum cover possible to protect the pipe from frost or crushing from the surface 	activity.

No transition from one pipe size to another or from one pipe material to another shall be 	made without the use of manufactured adaptors designed specifically for that purpose.  	All changes in direction shall be made with pipe fittings not greater than 45 degrees.  	Under certain conditions acceptable to the Authority, sweep 90 degree bends may be used 	and shall be so noted on the connection permit.

C.  PRESSURE LATERAL – The pressure lateral shall include the redundant check 	valve provided by the Authority.  This valve shall be located three feet from the curb 	stop.  The pressure lateral shall be 1 ½ -inch SDR 21 PVC (200 psi), pipe with rubber 	gasket joints, buried a minimum of four feet.  Thrust blocks shall be provided for all 	fittings and at all locations where horizontal and/or vertical deflections are made.

- Earth dams shall be provided in the pressure lateral trench for the purpose of stopping the natural flow of water.  Earth dams shall be constructed at no greater than 50’ intervals.  All laterals constructed from layers of compacted soil.   The soil shall be placed by hand and compacted with tools designed for this purpose.

As a minimum the soil shall be placed and compacted in the following three layers:

A.  At pipe bottom

B.  On the pipe sides

C. 12 inches above the top of the pipe

D.  Bedding Material Requirements for Sewer Pipe – All types of pipe shall be bedded 	with five (5) inches of bedding material and backfilled with approved bedding material 	that is thoroughly compacted to a depth of at least 12” above the top of the pipe.

1.  Bedding material shall conform to AASHTO number 8, or commonly known 			as PA 1B crushed aggregate, in accordance with the Pennsylvania Department of 			Transportation’s Specifications.

2.  After the pipe has been installed, jointed, inspected and tested, the trench shall 			be backfilled with bedding material.  Backfill from the top of the pipe to a depth 			of twelve (12) inches over the pipe and the bedding material shall be as specified 			herein.

From twelve (12) inches over the pipe to the elevation of final grade, backfill material 	shall be placed in uniform even twelve (12) inch layers and each layer shall be carefully 	and thoroughly compacted by hand operated mechanical tampers.  Backfill material 	within these layers may be placed by machine providing sufficient personnel are utilized 	to properly spread the material, to prevent the inclusion of objectionable material and 	attain complete compaction.

Backfill material from twelve (12) inches over the pipe to final grade shall be the material 	removed from the trench with the exception that no organic material or rock larger than 	six (6) inches shall be included in the backfill.

E.  Service Lines shall be laid on a grade of not less than one-quarter of an inch per foot 	(2%) for four inch pipes and one-eighth of an inch per foot (1%) for six inch pipes or 	larger.  Pipe slopes less than 2% can only be installed accurately with pipe laser and must 	be approved by the Authority.

F.  Service Lines must be as direct as possible.  Changes in direction must be made with 	“Y’s”, 	combination “Y” and eighth bends or half “Y’s”, or one-eighth bends.  Any 90 	degree change in direction shall include a clean out.  Changes in size where the Lateral 	Sewer is connected to the Service Line shall be made only with fittings.

G.  Ditches shall be promptly backfilled after inspection and approval by the Plumbing 	Inspector.  Care shall be taken to prevent damage to the pipe in backfilling and to secure 	a well compacted and firm trench.

H.  On existing improved properties as distinguished from future properties to be improved the Service Line shall be vented, trapped, and an inspection port be placed on the line beyond the building.

1.  Vents – Except those properties that are properly vented a vent shall be placed 			along the house sewer line at a location acceptable to the plumbing inspector.  			Vents risers shall extend a minimum of twelve (12) inches above the ground 			surface and shall be capped with a mushroom vent or double bend.  Vents shall be 		at least four inches in diameter.

2.  Traps – Each building shall be provided with a main building trap.  The trap 			may be located wherever possible within the cellar of the building or immediately 		outside the building wall.  Note:  The vent should be placed upstream of the main 			building trap.

- Clean-outs – A clean-out shall be placed immediately following the building trap and at every 50-foot interval along the building sewer.  Clean-outs shall also be provided at every change in direction which exceeds 45 degrees.  The clean-out shall consist of a wye fitting in the run of pipe with a 45 degree bend and riser to the ground surface.  The riser pipe shall be provided with a metal panella and removable plug.

- Inspection Port – An inspection port shall be placed at or near the septic tank.  The Authority is only responsible for the building sewer from the inspection port to the septic tank and to the sewer mains.  The sewer lateral from the building to the said clean-out is the sole responsibility of the property owner.

Solids retaining tanks shall be constructed of concrete and shall be watertight.  An inlet baffle 	shall be provided and shall extend a minimum of six (6) inches below the top of the liquid level.  	Outlet port is to be equipped with a vented tee which extends below the liquid level to a distance 	equal to 40% of the liquid depth.  Each tank shall contain a six (6) inch inspection port located 	overtop the inlet baffle and minimum twenty (20) inch access port.  Inspection port is to extend 	to finish grade. Access port is to extend to twelve (12) inches below grade using precast concrete 	riser rings.

Tank sizing to be in accordance with the following:

EDU			TANK SIZE

1-2			1000 Gal.

3-5			2000 Gal.

6-12			4000 Gal.

Tank bedding requirements:

1.  1000 and 2000 gallon tanks

A.  Six (6) inches of select granular material

2.  4000 gallon tank

A.  Set tanks on a six (6) inch poured in place concrete slab.

B.  Pour slab over top of a minimum six (6) inch bed of select granular 				material

3.  All bedding material to be thoroughly compacted using mechanical tamping 			equipment.

The tank depth shall be determined by the Possum Valley Municipal Authority.

I.  A complete grease recovery unit as manufactured by Lowe Engineering Co., 	Thermaco, Inc, or equivalent shall be installed in the building sewer of restaurants and 	other commercial facilities involved in the preparation of food.  The grease recovery unit 	design must be submitted to the Authority and its consulting engineer for approval.

J. Basement floor drains may not be connected to the building sewer, except by special 	permission of the Authority, and if permission is granted by the Authority, the property 	owner(s) must assume the risk and expenses of having the basement floor drain 	disconnected at a later date because of ground water entering the building sewer and 	sewer system.

K.  The Authority reserves the right to require air testing for service lines.  The procedure 	for air testing is as follows:

Low-Pressure Air Tests – The sewer customer shall test each service line using low 	pressure air.  The low pressure air test shall be at 5 psi for 5 minutes.  All inflatable plugs 	shall be adequately braced for safety reasons.

A minimum period of 2 minutes shall be provided to allow equilibrium of the air 	temperature with pipe wall before test reading shall commence.  In areas of high ground 	water conditions, the contractor shall determine the height of the ground water, and an 	adjustment may be required by the Authority Representative.

The contractor shall submit to the Authority for approval of the test procedure and list of 	test equipment he proposed to use prior to testing.

L.  Upon completion of each Service Installation, the Plumbing Inspector is to be notified 	and an appointment made for inspection.  All pipes and pipe joints must be visible and 	accessible to the Plumbing Inspector.  If the work is satisfactory, the permit, which must 	be on hand at the time of the inspection, will be endorsed and returned to the Owner.

SECTION II

SOLIDS RETAINING TANKS & PUMPING STATIONS

Should an improved property be required by the Authority to install a sanitary sewer 	solids retaining tank and/or a pumping station for collection and conveyance, the owner 	and its 	successors shall have full responsibility for using the pump station consistent with 	the manufacturer's instructions and shall avoid introducing into the wastewater system, 	materials that may damage the pump, conveyance system, and collection system or 	treatment facilities.  Furthermore the owner, at their own cost, will have the septic tank 	pumped on intervals as set forth by the Authority.

The Authority shall bear no responsibility for the purchase, 	installation, use, operation, 	maintenance, service, repair, or replacement of the pump station or any component part 	thereof on the Property, except as otherwise set forth herein or as required by law.

Responsibility for already existing commercial property pump stations and septic tanks 	that are connected to the Authority’s system will be transferred to any new owner or 	successor for the improved property.

SECTION III

CAPITAL CHARGES FEE FOR SEWER SERVICE

A.  In addition to a permit, this Authority does hereby charge a Capital Charges fee, in 	the amount set forth in Paragraph B, hereof, against the Owner of any Improved Property, 	whenever such Owner hereafter shall connect any such Improved Property with a sewer 	main constituting a portion of the Sewer System, such charge being authorized by the 	Municipal Authorities Act.  Such Capital Charges fee is charged for connection of each 	such Improved Property by the Owner of such Improved Property.

B.  The amount of the Capital Charges fee for connection of each Improved Property to 	the Sewer System shall be in accordance with the Municipal Authorities Act and shall be 	subject to the rules and regulations in effect at time of connection.  Properties not 	intended to be served as part of the original contracts for construction will pay the stated 	Capital Charges fee in addition to any cost incurred by the Authority to provide service to 	the property.

The Capital Charges fee for municipal sewerage shall be on an EDU (Equivalent 	Dwelling Unit) basis and shall be in accordance with the most recent version of the 	Possum Valley Municipal Authority’s Capital Charges Study Pursuant to the Municipal 	Authorities Act.  Each EDU shall be represented by a volume of wastewater generated by 	a typical residential dwelling unit as stated in the most recent Chapter 94 Report as 	prepared annually in accordance with the Pennsylvania Department of Environmental 	Protection.  The EDU’s for Non-Residential Units will be billed as per the category as 	listed in Section IV, Paragraph B, or will be based on metered rate.  Example:  If a 	business or professional office has one hundred (100) employees, this would constitute 	10 EDU’s.  Therefore the connection fee would be ten (10) times the amount to be paid 	by a typical single family residential unit.

C.  The Capital Charges fee and permit fee, together with any estimate of additional costs 	shall be due and payable at the time application is made by the Owner of any property to 	the Authority for a permit to connect such property with the Sewer System.  In the case 	where a Planning Exemption or Planning Module for Land Development is required, the 	Capital Charges fee will be payable upon approval of the Planning Module or Exemption 	and allocation of the requested capacity.

D.  The Capital Charges fees, permit fees, and costs shall be made payable to the Possum 	Valley Municipal Authority or representative of this Authority as shall be authorized 	from time to time, by resolution of the Authority, to accept payment thereof.

E.  The Authority reserves the right to periodically re-evaluate the User Classification of 	any customer.  If additional capacity is being used the Authority reserves the right to 	assess any additional capital charges due.  Evaluations are determined by, but not limited 	to, the proceeding Equivalent Category Schedule or if applicable the peak quarterly water 	usage for the year.

SECTION IV

SEWER RENTAL OR CHARGES

Sewer rentals or charges are imposed upon and shall be collected from the Owner of each Improved Property which shall be connected to the Sewer System, for use of the Sewer System, whether such use shall be direct or indirect, and for services rendered by the Authority which shall commence and be effective as of the date of connection of each Improved Property to the Sewer System, and shall be payable as provided herein, in accordance with the adopted schedule of rates and classifications as follows:

A.  Residential

Each Private Dwelling Unit shall be charged a monthly rate, billed monthly, rate to be 	determined by the Authority on a yearly basis.  Each Dwelling Unit in a double house or 	in a row of connected houses or in an apartment building shall be billed as a separate 	entity.  If two or more families use separate cooking and/or toilet facilities in an 	Improved Property, the sewer rental or charge payable hereunder shall be computed as 	though each such family was a separate user with a separate connection to a sewer.

B.  Non-Residential (Commercial, Industrial, Schools, Clubrooms, Taverns, Fire Houses, 	Professional Offices, Hotels, Restaurants, Churches, Service Stations, Garages, Barber 	Shops, Beauty Shops, Laundromats, Institutions, etc.):

1.  All Owners of non-residential Improved Properties connected to the Sewage Collection 	System shall pay a Rental at the rate as set forth in the following schedule:

Equivalent Category Schedule			Monthly Rate

1.  Each Retail Store…………………………..………up to 10 Employees = 1 EDU

2.  Each Business or Professional Office……………..up to 10 Employees = 1 EDU				3.  Each Business or Professional Office……………..up to 10 Employees = 1 EDU

attached to Building for Public Transactions

4.  Each Hotel, Motel or Boarding House…………….2 Rooms = 1 EDU

(in addition to restaurant)

5.  Each Restaurant, Club, Tavern…………………... every15 Employees or part thereof   = 1 EDU

every 15 Seats or part thereof = 1 EDU

6.  Each Church………………………………………. = 1 EDU

with Kitchen Facilities = *

7.  Each Service Station or Auto Repair…………..….Garage Only = 1 EDU

Garage with Car Wash = 3 EDU

8.  Each Car Wash…………………………………….1 Bay = 2 EDU

9.  Each School (Students & Employees)………….…up to 18 Persons = 1EDU

10. Each Laundromat………………………………...2 Washing Machines (Single Load) = 1 EDU

2 Washing Machines  (Double Load ) = 1.5 EDU

11. Each Bowling Alley……………………….……..5 Lanes = 1 EDU

12. Each Barber of Beauty Shop………………….….2 chairs or less = 1.5 EDU

Each chair over 2 = 1 EDU											if attached to a residence

For both (2 chair maximum) = 2 EDU

13. Each Industrial Establishment…………..………..	Up to 10 Employees = 1 EDU

(excluding process waste)

14. Hospitals…………………………………………..Up to 10 employees = 1 EDU

2 Beds = 1 EDU

15. Nursing Homes………………………………..….Each Bed = 1 EDU

16. Personal Care Homes……………………..………Each 2 Residents = 1 EDU

17. Each Fire Company with Social Hall………..……= 1 EDU

with Kitchen Facilities = *

18. Convenience Store, Combination, Gas/Grocery… = 3.5 EDU

19. Each Day Care Center……………………………3 through 9 Non Related Children = 1 EDU

Each Additional 6 Children = 1 EDU

* To be evaluated annually by The Authority based on the peak quarterly average flow for any given year.

2.  Sewer rentals and charges for schools payable hereunder shall be computed on 			the basis of the estimated number of pupils for purposes of this calculation.

3.  Sewer rentals and charges for businesses or industrial units payable hereunder 			shall be computed on the basis of the number of employees (including individual 			owners and employers and/or seats) as reported on Form 941 for the quarter 			ending September 30th of each year.

4.  If the Owner of any non-residential Improved Property (including any school) 			shall fail to return to this Authority its “Category Classification Form” by 				November 15th of each year with complete information required to compute the 			sewer rental and charge to such non-residential Improved Property, this Authority 			may estimate a reasonable applicable sewer rental and charge for such non-			residential Improved Property  such estimated sewer rental and charge shall be the 		actual sewer rental and charge payable until the required information is filed;  			provided, however, that no rebates will be paid by this Authority if the 				information filed reveals a lower indicated sewer rental and charge than that 			estimated by this Authority.

C.  If two or more Dwelling Units, stores, offices, industrial units, etc. are connected to 	the Sewage Collection System through a single Lateral; or if two or more types of use are 	made of the same Improved Property, the Sewer Rentals and charges payable hereunder 	shall be computed as through each such Dwelling Unit, store, office, industrial unit, etc. 	and each such type of use were a separate Improved Property or user with a separate 	connection to a Sewer.

D.  Additional classifications and Sewer Rentals or modifications of the above schedule 	of sewer rentals charges may be established by this Authority for time to time as deemed 	necessary.

E.  Nothing herein contained shall be deemed to prohibit this Authority from entering 	into separate agreements with Owners (including any school) with respect to Sewer 	Rentals to be imposed in those cases where, due to seasonal fluctuations or other unusual 	circumstances, the Sewer rentals or charges set forth herein shall be deemed by this 	Authority to be unfair or inequitable.

F.  The connection fee and permit fee, together with any estimate of additional costs shall 	be due and payable at the time application is made by the Owner of any property to the 	Authority for a permit to connect such property with the Sewer System.

G.  All connection fees, permit fees, and costs shall be made payable to the Possum 	Valley Municipal Authority or representative of this Authority as shall be authorized, 	from time to time, by resolution of the Authority, to accept payment thereof.

TIME AND METHOD OF PAYMENT

A.  All bills for sewer rentals or charges shall be rendered on the first day of each month, 	in each year, or on such other dates as this Authority by resolution shall specify, and shall 	cover a monthly billing period consisting of the immediately preceding month.

All bills for sewer rentals or charges based on estimates of this Authority shall be 	rendered for each month promptly after the estimates are made.

Owners of Improved Properties connected to the Sewage Collection System during any 	month shall pay a pro rata sewer rental or charge for service for the balance of that 	month.

B.  Sewer rentals or charges shall be due and payable upon the applicable billing date as 	provided for in subsection A of this Section III and the appropriate amount computed in 	accordance with this Resolution shall constitute the net bill.  If sewer rentals or charges 	are not paid within 30 calendar days after each billing date, an additional sum of $10.00 	shall be added to such net bills, which net bill, plus such additional sum shall constitute 	the gross bill.  Payment made or mailed and postmarked on or before the last day of such 	30 calendar day period shall constitute payment within such period.  If the 	end of such 30 	calendar day period shall fall on a legal holiday or a Sunday, payment made on or mailed 	and postmarked on the next succeeding weekday which is not a legal holiday shall 	constitute payment within such period.  Any bill not paid within said 30 day period shall 	be deemed delinquent, and will accrue interest at 2% per month.

CHANGE IN ADDRESS, OWNERSHIP OR TENANCY

A.  Every Owner of Improved Property which is connected to the Sewage Collection 	System initially shall provide this Authority with and thereafter shall keep this Authority 	advised of his correct address.  Failure of any Person to receive bills for sewer rentals or 	charges shall not be considered an excuse for nonpayment nor shall such failure result in 	an extension of the period of time during which the net bill shall be payable.

B.  Every Owner of Improved Property which is connected to the Sewage Collection 	System shall advise the Authority in writing on any change of ownership or tenancy of 	the Improved Property.  Failure to provide notice libels the initial property owner for any 	sewer rentals or charges that may accrue until such time as the Authority has been 	notified of an ownership or tenancy change.

ENFORCEMENT

Any person, partnership, corporation, or other legal entity who shall violate these Regulations shall be required to make restitution equal to the costs of repair or replacement of damaged Authority equipment.  Restitution shall not be limited to materials only but shall also indicate labor or time required for fact finding investigation into the cause of the damage together with reasonable attorney fees for enforcement.  Multiple offenses of these regulations shall warrant an additional $500 as part of said restitution.

The connection fees, surcharges, sewer rental fees, restitution fees, and/or penalty charges imposed by this Authority shall be a lien on the improved property connected to and served by the sewer system where such fees or charges are not paid as provided herein, which lien shall be filed in the Office of the Prothonotary of Adams County, Pennsylvania, as the case may be, and shall be collected in the manner provided by law for the filing and collection of municipal claims.  In addition, the payment of said fees imposed hereunder may be enforced by the Authority in any manner appropriate under existing laws at the time they 	become due and payable.

SECTION V

ADDITIONAL PROVISIONS OF THIS RESOLUTION

A.  This Resolution shall become effective immediately upon date of adoption.

B.  Any Sewer rentals or charges deemed delinquent, pursuant to this Resolution, shall be 	cause for termination of service and shall be collected in any manner appropriate under 	laws at the time in effect.

C.  This Authority reserves the right to adopt, from time to time, such additional rules and 	regulations as it shall deem necessary and proper in connection with use and operation of 	the Sewage System, which rules and regulations shall be, shall become and shall be 	construed as part of this Resolution.

D.  This Authority shall in accordance with applicable federal guidelines, provide for 	annual review and revision of all user charges and revise them periodically, if necessary, 	to meet actual operation and maintenance expenses and records shall be maintained as are 	necessary to document compliance with future regulations on the Authority’s user 	charges.

E.  In the event any provision, section, sentence, clause or part of this Resolution shall be 		held to be invalid, such invalidity shall not affect or impair any remaining provision, 	section, sentence, clause or part of this Resolution, it being the intent of this Authority 	that such remainder shall be and shall remain in full force and effect.

Adopted and approved this________________________________

POSSUM VALLEY MUNICIPAL AUTHORITY

Michael A. Johnson, Chairman

Attest:  _________________________________Harry M. Melhorn, Secretary/Treasurer